Catalog Part No:	QA-72C-RM (1x size – image on photographic paper)

Product Name:ISO-12233 Low Contrast Edge SFR chart with 80:1 OECF Patches

Drawing / Photo of part:

The above image is an approximate representation of the actual product.
Specifications are subject to change without notice.

Description:

This test pattern is an image evaluation tool for determination of resolving power, limiting resolution and spatial frequency response (SFR) of digital images systems at a low contrast signal point. The central OECF grayscale patches can be used to evaluate linearity. It is as specified in ISO 12233:2014,  Annex C.

Sizes and Image Forming Material:

| Part Number | Size | Substrate Size (mm) | Active Image Area (mm) | Substrate Type | Image Forming Material |
| --- | --- | --- | --- | --- | --- |
| QA-72C-P-RM | 1X | 240 x 340 | 200 x 300 | Photographic paper | Photographic emulsion |

Image Description:

The  ISO-12233 Low Contrast Edge SFR chart with 80:1 OECF Patches  contains a variety of test pattern elements.  Users are advised to refer to International Standard ISO-12233 for a detailed explanation of the target’s features and their use.  The following is a summary list of image features.

- Framing arrows, which define, 4:3, and 3:2  aspect ratios, assist in framing the target’s active area.

- A central multi-frequency zone plate on a black square can be used to set focus.

- Slightly slanted squares (approximately 5°) provide spatial frequency response (SFR) at multiple locations.

Polarity:  Positive image features

Image Contrast: The background reflectance is between 15% R and 25% R.  The modulation of the slant edge test areas (relative to the background) is between 0.55 and 0.65.

The modulation calculation method is;   Rmax- Rmin / ((Rmax+Rmin)/2)

Terms:

- Aliasing – The appearance of image artifacts due to limited or diminished resolution.

- Aliasing ratio – The quantity of image distortion due to aliasing expressed as the ratio of maximum minus minimum response to the average response within a burst pattern (a series of line and space features at a slight angle to the image sensor).

- Image aspect ratio – The ratio of image width to image height.

- Resolution – The measure of a camera or imaging component to convey detail.

- SFR (Spatial Frequency Response) – The amplitude response of an imaging system as a function of relative spatial frequency.

- Spectrally neutral – Spectral power distributions of equal value.

Guidelines for Usage:

This document is not intended to replace the International Standard Document ISO-12233.  However, the following guidelines will aid the first use of this chart.

- The chart should be illuminated uniformly (±10% of center luminance) against a surround of low reflectance and with a minimum of flare light.  The illuminant should be effectively neutral with respect to either daylight or tungsten illuminants (ISO-7589).  Camera white balance should be adjusted to provide equal red, green and blue signal levels.

- The camera should be positioned to provide centered, full-frame-height rendering of the chart’s active area.  Use the chart’s framing arrows and horizontal edges to aid positioning.  The camera to test chart distance should be noted.

- Use the chart’s central zone plate feature to set good focus.

- Set camera lens aperture and exposure time to provide maximum signal from white areas while avoiding any signal clipping.

- Where possible, image compression features should be disabled.

- Camera output signal should be linearized using the standard reflection camera OECF (Opto-Electronic Conversion Function) test chart, Applied Image part number ST-52-RM, or the test patches provided on this chart.

- Line width features can be viewed with any file viewer for an indication of the visual resolution limits of the device.  International Standard Document ISO-12233 contains instruction regarding a quantitative determination of resolution limits.  Visual and limiting resolution values should be reported in values of lw/ph.

Slant-edge features can be analyzed using SFR software  available through:

Windows and Mac  SFR program (sfr.zip) is available at no charge from:

Image Quality from an Edge Target (SFR)

http://www.mitre.org/tech/mtf/index.html

ImageJ is a handy image analysis tool, with many plugins, including one for mtf analysis;

https://imagej.net/Welcome

https://imagej.net/plugins/se-mtf/index.html

Sourceforge offers a “pre-alpha” version of SFR analysis at:

http://sourceforge.net/projects/slantededge/

Sourceforge also has;

http://sourceforge.net/projects/mtfmapper/

Not free, but decent analysis program:

http://www.quickmtf.com/

- This topic is also described in greater detail in the International Standard Document ISO-12233.

Related Information:

- International Standard Document ISO-7589, Illuminants for sensitometry – Specifications for daylight and incandescent tungsten

- International Standard Document ISO-12233, Electronic still-picture cameras – Resolution measurements

- International Standard Document ISO-14524, Electronic still-picture cameras – Methods for measuring opto-electronic conversion functions (OECFs)

Related Applied Image Products:

- M-13-60; Sinusoidal Array.  Sinusoidal test images evaluated for MTF (Modulation Transfer Function) are the classic means of imaging quality evaluation.  (MTF is comparable to SFR evaluation.)

- QA-61; Reflective Scanner Test Chart (ISO-16067-1).  Designed for scanners, this chart contains a slanted edge feature for SFR evaluation.  Additional features are included for resolution, aliasing ratio and OECF testing.

- QA-62; Slant Edge Target.  Designed for scanners, this chart contains a slanted edge feature for SFR evaluation along with an OECF grayscale in a single target.

- QA-76; Digital CINE Resolution Chart.  Based on the ISO-12233 chart, the QA-76 has extended width for devices having higher aspect ratios.

- QA-77; Enhanced Digital Camera Resolution Chart.  This target is based on the ISO-12233 chart but allows determination of resolution limits as high as 4000 lw/ph.  Lower contrast slant edge features provide more accurate SFR analysis.

- QA-72 Digital Still Camera Resolution Chart

- QA-72A ISO 12233 CIPA Resolution Chart.